## Slide 1: Spiking Neural network accelerator in a heterogenous system with CNN and SNN
Training of CNN-SNN system using SnnTorch and RTL implementation of SNN Inference
Supervisor : Prof. Alberto Garcia-Ortiz
Presented by : Maya Ambalapat

## Slide 2: Contents
Motivation
Goals
Background
  Spiking Neural Network
  Spiking neuron models
  Spike encoding techniques
  SNN Training
Implementation
  Training CNN-SNN complementary network using PyTorch and SnnTorch
  RTL Design of SNN core
  RTL Simulation Result
Conclusion
Scope
References

## Slide 3: Motivation
State-of-the-Art AI has high power consumption
Brain consumes only 20W of power
Bridge this difference in power consumption
Biologically inspired spiking neural Networks
Low power, dynamic Applications

## Slide 4: Motivation
Data is transmitted as spikes instead
of high precision values.
Accumulation operations replace MAC operations
Online learning possible
Low accuracy compared to CNN

## Slide 5: Motivation
Take advantage of complementary
properties of SNN and CNN
Workload division based on sparsity
SNN efficient when
spike sparsity > 97.7%

## Slide 6: Motivation
CNN has spatially arranged full adders
even if the operand is small, a large number of full adders are operated, and the computational power remains constant.
For large amount of small data, SNN with low computational power consumption is useful.
For a lot of large-magnitude data, CNN with low-power variation is useful.

## Slide 7: Goals
Implement RTL design of SNN inference module and scratchpad controller.
Training of SNN-CNN heterogenous system using PyTorch and SnnTorch
Verify the RTL design functionality
Synthesis of RTL design

## Slide 8: Spiking Neural Network
Sparsification over time
Less computation
Fewer memory lookups
Event driven processing
Asynchronous
Training is difficult
Tradeoff between Accuracy and power consumption

## Slide 9: Neuron models
Leaky Integrate and Fire Neuron model(LIF)
  Simple and commonly used
  Fits data better than the realistic models
  [1] shows that the simpler IF model is more energy-efficient than the Leaky IF and temporal continuous synapse models. Moreover, SNNs with the IF model can compete with efficient ANN implementations when there is a very high spike sparsity,
Hodgkin-Huxley model
  biophysically accurate models
  complexity makes them difficult to use

## Slide 10: Leaky Integrate and Fire (LIF) neuron
For each time period t:
  Update Neuron Voltage(V)
  Process any incoming spike
  if V crossed the Vth, emit a spike and reset V
V[t+1] = β*V[t] + W*X[t+1]-S[t]Vth
S[t] = 0 if V[t] > Vth else 1

## Slide 11: SNN encoding techniques
Static Non-spiking dataset
time-varying sequence of spikes
Rate encoding
Latency encoding

## Slide 12: SNN Training
STDP
  Works for shallow models
  Hardware friendly
ANN to SNN conversion
  Appropriate threshold selection
Backpropagation using surrogate gradient

## Slide 13: Training CNN-SNN complementary network using PyTorch and SnnTorch

## Slide 14: Training CNN-SNN complementary network using PyTorch and SnnTorch
Google collab
CNN only model ,
  Accuracy of 90.63%
CNN-SNN model,
  Accuracy of 89.7%
Leaky neuron properties
  Beta = 1 , no Leak in Voltage
  Threshold = 1 (default value)
  Time steps = 12

## Slide 15: CNN-SNN complementary model

## Slide 16: Training CNN-SNN complementary network using PyTorch and SnnTorch
Collect data from trained model
INT8 Quantization of weights using Brevitas
Input and output spikes of SNN layer is stored to a file

## Slide 17: CNN-SNN complementary system
SNN Core
  Distributed cache system
  Spike encoding
  Accumulator to add weights based on input spikes

## Slide 18: RTL Design of SNN core

## Slide 19: Advantages
Weight Reuse
  Distributed cache system
  the power consumption of the SNN
  core decreases by 42.2% and 49.1%
  for ImageNet classification with ResNet-18 and MobileNet

## Slide 20: RTL Simulation Result

## Slide 21: Result Verification
Output spike of VHDL simulation is stored to a file.
It is then compared with the output spikes of SNN layer in PyTorch using a Python script.

## Slide 22: Conclusion
Energy efficiency:
  15%–31% for CIFAR-10
  15%–38% for CIFAR-100
  11%–50% for ImageNet

## Slide 23: Conclusion
Low power inference using heterogenous systems has higher energy efficiency than SNN-only or CNN-only mode.
RTL design of SNN inference module have been implemented.

## Slide 24: Scope
Implementation of online learning in hardware
The RTL design of inference module can replace the CNN core in Gemmini accelerator
Thus the system can be configured to work as a heterogenous SNN-CNN accelerator

## Slide 25: Questions

## Slide 26: References
Manon Dampfhoffer, Thomas Mesquida, Alexandre Valentian, Lorena Anghel. Are SNNs really more energy-efficient than ANNs? An in-depth hardware-aware study. IEEE Transactions on Emerging Topics in Computational Intelligence, 2022, 2022, pp.1-11. ff10.1109/TETCI.2022.3214509ff. Ffcea03852141f
J. K. Eshraghian et al., "Training Spiking Neural Networks Using Lessons From Deep Learning," in Proceedings of the IEEE, vol. 111, no. 9, pp. 1016-1054, Sept. 2023, doi: 10.1109/JPROC.2023.3308088.
S. Kim et al., "C-DNN: An Energy-Efficient Complementary Deep-Neural-Network Processor With Heterogeneous CNN/SNN Core Architecture," in IEEE Journal of Solid-State Circuits, vol. 59, no. 1, pp. 157-172, Jan. 2024, doi: 10.1109/JSSC.2023.3330483.

## Slide 27: Images
Gosciniak, Jacek. (2021). Plasmonic nonvolatile memory crossbar arrays for artificial neural networks. 10.48550/arXiv.2107.05424.
Huang, Anping & Zhang, Xinjiang & Li, Runmiao & Chi, Yu. (2018). Memristor Neural Network Design. 10.5772/intechopen.69929.

## Slide 28: Thank you